## Slide 1: GPU programming
Geert Jan Bex
(geertjan.bex@uhasselt.be)
License: this presentation is released under the Creative Commons CC BY 4.0, see https://creativecommons.org/licenses/by/4.0/deed.ast

## Slide 2
https://github.com/gjbex/GPU-programming

## Slide 4: Typographical conventions
Good practice:
Bad practice:
(Potential) hazards/bugs:
Performance issue:
Performance boost:
Warning:

## Slide 5: What do GPUs look like?

## Slide 6: Host-device model
Compute node has
  1 or more CPUs
  Volatile memory: RAM
  PCIe bus with
    1 or more GPUs
Application
  Runs on host
  Offloads computations to device(s)
Host
Device(s)

## Slide 7: Offload model
Host
Device0
Device1


## Slide 8: Host-device model implications
Explicit data transfer between host and device
Explicit synchronization
  Avoid race conditions
Interconnect latency/bandwidth
  Potential performance bottleneck
Hardware details matter a lot!

## Slide 9: GPU hardware

## Slide 10: Terminology crosswalk
Concept | NVIDIA/CUDA | AMD Instinct/HIP
Compute unit | Streaming Multiprocessor (SM) | Compute Unit (CU)
Execution subgroup | Warp, 32 threads | Wavefront, 64 work items
Cooperative thread group (work-group) | Thread block | Work-group/thread block
Work-group local scratchpad | Shared memory | Local Data Share (LDS)
Register resources | Register file | Scalar & vector registers (SGPR/VGPR)
Matrix accelerator | Tensor core | Matrix core/MFMA
Architecture target | Compute capability | GFX target
GPU interconnect | NVLink/NVSwitch | Infinity Fabric/xGMI
Collective library | NCCL | RCCL

## Slide 11: Compute unit execution model
SIMT: Single Instruction, Multiple Threads
  threads grouped in execution subgroups
  Threads in subgroup execute same instruction on different data
Branching
  Cheap if threads in subgroup agree
  Divergence leads to
    Masking of inactive threads
    Execution of both paths
  Try to avoid branching
    Code structure
    Data layout
Execution subgroups grouped in work-groups
 performance loss

## Slide 12: Compute unit
Instruction schedulers select ready execution subgroups
Simple architecture
  No complex per-thread CPU-style execution
  Latency hiding: many resident execution subgroups
Pipelines for
  Floating point
  integer
  Matrix acceletion
Load/store units
Register resources (thread-private)
Hardware managed local cache
Work-group local software managed scratchpad
Registers
Scratchpad
Cache
Scheduder
Scheduder
FP pipeline
INT pipeline
Matrix accelerator
LD/ST
Compute unit

## Slide 13: Matrix accelerators
Computed as many small tiles
  C
Tile size depends on
  Data type
  Architecture target
Performance: matrix accelerators TFLOP/s >> compute unit TFLOP/s
where , B

## Slide 14: Multiple compute units
GPU has many compute units
Connected to device memory fabric
  Device-level cache(s)
  Devide-level memory
Massive parallelism!

Cache
Memory
GPU

## Slide 15: Memory hierarchy
Meory resource | Conceptual scope/role | Managed by
Register resources | Active work item, subgroup state | Compiler and hardware
Work-group local scratchpad | Visible to work-group | Program
Hardware-managed local cashes | Accelerate memory access near CU or CU cluster | Hardware
Device-level cache (L2) | Serves all CUs | Hardware
Device-level memory | Accessible to all work-groups | Program/runtime
Latency
Size
Latency hiding through oversubscription
Registers + scratchpad  resident work-groups, work-times per group

## Slide 16: Multiple GPUs/node, multiple nodes
Typically, 4-8 GPUs/node
  Connected via GPU interconnect
  PCIe connection to host
Nodes connected via high-bandwidth/low-latency network interconnect

CPU(s)
Host memory
Node


## Slide 17: Bandwidth hierarchy
Path | Illustrative peak performance | Relative to GPU device memory
GPU device memory (HBM) | 1.5–8 TB/s | 1 
GPU to GPU interconnect | 300–900 GB/s per GPU, one way |  0.08–0.15 
Host memory | 200–500 GB/s per CPU socket |  0.05–0.2 
PCIe | 32 GB/s (Gen4), 64 GB/s (Gen5) one way |  0.01–0.04 
Interconnect network | 12.5–50 GB/s per port, one way |  0.003–0.03 
Minimize data transfers
Host-GPU
GPU-GPU
Node-node

## Slide 18: Programming models

## Slide 19: How to express GPU work?
Prebuilt operations  mathematical operations
  E.g., matrix multiplications, linear solver
Pattern-based programming  parallel patterns & execution policies
  E.g., Kokkos: parallel for, reduction
Directive-based programming  annotated loops & data environment
  E.g., OpenMP target
Kernel-oriented programming  explicit kernels, launches, memory, dependencies
  E.g., CUDA, HIP
More implementation details, more fine-grained control
More portable

## Slide 20: Memory management
Explicit memory management
  Memory allocation/deallocation
  Host versus device addresses
  Explicit copy
    Host  device
    Device  host
    Device  device
  Explicit synchronization
Unified memory management
  Memory allocation/deallocation
  Single address space
  Implicit data migration (page fault/page copy)
  Explicit synchronization
More control, potentially better performance

## Slide 21: Kernels
Functions compiled for device
Operate on data in device memory
Launched from host, run on device
Configuration in 1D, 2D, 3D
  Threads per block
  Blocks per grid

## Slide 22: Threads, blocks & grid
Threads per block: x-dimension  y-dimension  z-dimension  1024
  x-dimension  1,024
  y-dimension  1,024
  z-dimension  64
Blocks per grid
  x-dimension  231 - 1
  y-dimension  65,535
  z-dimension  65,535
Warp is 32 threads, warp-group is 4  32 threads
Kernel can get
Thread indices, thread dimensions
Block indices, block dimension
 differentiate work/thread
Numbers for NVIDIA H100, query the device!

## Slide 23: Streaming Multiprocessors & blocks
All threads in block execute on same SM
  Can be synchronized
  Can use shared memory
Multiple blocks assigned to SM
  Depends on registers, shared memory/L1 cache availability
Threads grouped in warps
  At most 64 warps resident on SM
4 warp schedulers  at most 4 warp instructions/cycle
  Need not belong to same block
  Picked from ready warps
  Number of instructions depends on pipelines used
Stalled warps: waiting for
  Memory
  Synchronization
  Long-latency instructions
Many threads/blocks  latency hiding
Numbers for NVIDIA A100, query the device!

## Slide 24: Synchronization
Memory copy can be asynchronous
Kernel execution can be asynchronous
Synchronization levels
  Subgroup: implicit lockstep execution  synchronization
  Block: explicit sync statement
  Cluster (NVIDIA H100+): cluster boundaries
  Grid: cooperative group kernel (all blocks must fit on GPU)
  GPU: kernel boundaries
Overlapping
Data transfers
Computations
 Explicit synchronization to avoid race conditions!!!

## Slide 25: Inquiry functions & configuration
Compute capability
Hardware limits
  Number of devices
  Maximum number of threads/block & dimension
  Memory/cache sizes
  

## Slide 26: Performance considerations
Avoid warp divergence (beware of branching)!
Ensure threads have enough work
Increase arithmetic intensity
Number of threads/block  registers/shared memory
  Ensure sufficient occupancy
Exploit data locality (shared memory/L2 cache)
Minimize host-device memory transfers and synchronization
Memory access matters  data access coalescing
  Accommodate 128-byte memory transactions
  Warp should access consecutive addresses  grid-strided loops to distribute work
  Data should be aligned
  Data layout  thread access pattern (e.g., SoA vs. AoS)
Note: opposite of CPU multithreading wisdom!

## Slide 27: Evolution

## Slide 28: Multiple GPUs/node, multiple nodes
Typically, 4 GPUs/node (A100)
  NVLink
    Direct connection between all GPUs
    12 NVLink link/GPU  4 links to each GPU
    50 GB/s/link (bi-directional)  200 GB/s between GPUs (100 GB/s each way)
  PCIe connection to host
NVIDIA Infiniband connects nodes

## Slide 29: Multiple GPUs/node, multiple nodes
Typically, 4 GPUs/node (A100)
  NVLink
    Direct connection between all GPUs
    12 NVLink link/GPU  4 links to each GPU
    50 GB/s/link (bi-directional)  200 GB/s between GPUs (100 GB/s each way)
  PCIe connection to host
NVIDIA Infiniband connects nodes

## Slide 30: Bandwidth hierarchy
Global GPU memory  2 TB/s
NVLink  100 GB/s each way per GPU pair
PCIe  32 GB/s each way
Host memory  300 GB/s
HDR Infiniband  25 GB/s each way per port
CPU
GPU0
HBM
GPU1
HBM
GPU2
HBM
GPU3
HBM
RAM
PCIe
NVLink
CPU
GPU0
HBM
GPU1
HBM
GPU2
HBM
GPU3
HBM
RAM
PCIe
NVLink
HDR

## Slide 31: NVIDIA Streaming Multiprocessor (SM)
4 Warp schedulers
Simple architecture
  No out-of-order execution
  No branch prediction
  No sophisticated control flow
Pipelines for
  FP32
  FP64
  INT
  Tensor
  LD/ST
Memory lanes for pipelines
4-byte registers (thread-private)
Block shared memory/L1 cache
Const/texture cache
Warp-group instructions (NVIDIA H100+)
  4 warps participate in tensor instruction
  Accommodate larger tensor cores & matrix tiles
Warp
=
32 threads, all execute same instruction
Input | 
FP16 | 1688
BF16 | 1688
TF32 | 1688
INT8 | 16832
FP64 | 884
Input | 
FP16 | 1688
BF16 | 1688
TF32 | 1688
INT8 | 16832
FP64 | 884
E.g., for NVIDIA A100

## Slide 32: NVIDIA memory hierarchy
Level | Scope | Managed by | Typical latency | Size (NVIDIA A100)
Registers | Thread | Compiler |  1 cycle | 64 K  4 B per SM
Shared memory | Block | Programmer |  10-20 cycles | Up to 164 KB, part of 192 KB
L1 cache | SM | Hardware | 30-40 cycles | 
Const/texture cache | SM | Hardware |  constant | 8 KB
L2 cache | GPU | Hardware |  200 cycles | 40 MB
Global (HBM) | GPU | Programmer |  400-800 cycles | 40 or 80 GB
Registers + shared memory  threads per block
Latency hiding through oversubscription

## Slide 33: Architecture & compute capability
Model | Architecture | Compute capability | NVLink version | PCIe version | Base frequency (GHz) | Boost frequency (GHz)
P100 | Pascal | 6.0 | 1.0 | 3.0 | 1.33 | 1.48
V100 | Volta | 7.0 | 2.0 | 3.0 | 1.20 | 1.53
A100 | Ampere | 8.0 | 3.0 | 4.0 | 0.77 | 1.41
H100 | Hopper | 9.0 | 4.0 | 5.0 | 1.67 | 1.83
HGX B200 | Blackwell | 10.0 | 5.0 | 6.0+ | 1.80 | 2.00

## Slide 34: NVIDIA memory architecture
Level | P100 | V100 | A100 | H100 | HGX B200
Registers | 64 K  4 B | 64 K  4 B | 64 K  4 B | 64 K  4 B | 64 K  4 B
Shared memory | 64 KB | 96 KB | 164 KB | 228 KB | 228 KB
L1 cache | 24 KB |  |  |  | 
L1 + shared | Separate | 128 KB | 192 KB | 256 KB | 256 KB
Const cache | 8 KB | 8 KB | 8 KB | 8 KB | 8 KB
L2 cache | 4 MB | 6 MB | 40 MB | 50 MB | 126 MB
Global | 16 GB | 32 GB | 80 GB | 80 GB | 180 GB
Check cache size assumptions for kernels!

## Slide 35: NVIDIA SMs
Model | SMs | Cores per SM | Lanes (TF32/FP64/INT) | Tensor cores per SM | Tensor tile sizes
P100 | 56 | 64 | 64/32/64 | N/A | N/A
V100 | 80 | 64 | 64/32/64 | 8 (mixed FP16/FP32) | 4  4  4
A100 | 108 | 64 | 64/32/64 | 4 (FP16, BF16, TF32, FP64) | 16  8  8
H100 | 132 | 128 | 128/64/64 | 4 (FP8, FP16, BF16, TF32, FP64) | 64  64  16
B200 | 148 | 128 | 128/64/64 | 4 (FP4, FP6, FP8, FP16, BF16, TF32, FP64) | 64  64  32
E.g., for H100
FP32 peak  60 TFLOP/s
FP8 tensor peak  2000 TFLOP/s
32 lanes  1 warp instruction/cycle
64 lanes  2 warp instructions/cycle
128 lanes  4 warp instructions/cycle

## Slide 36: NVLink/NVSwitch & PCIe
Model | Links/GPU | GPU-GPU bandwidth (GB/s) each way | PCIe bandwidth (GB/s) each way
P100 | 4 | 20 to 40 (non-uniform) | 16
V100 | 6 | 25 (non-uniform) | 16
A100 | 12 | 100 | 32
H100 | 18 | 150 | 64
B200 | 18 | 900 | 64

## Slide 37: Impact on software
More memory  increase tile size
More L2 cache  ensure L2 locality
Tensor cores  exploit mixed precision
More instruction level parallelism  occupancy can decrease
Overlap memory transfer and computation
Profile!

## Slide 38: Unit conventions
GB = gigabytes